## Slide 1
Stig Griebenow - Thang Truong – David Lacoste - Rémi Goalard
M2M & LTE-M(5G)

## Slide 2
Introduction
MAC layer definition
Contention-based protocols
Scheduled protocols
Conclusion

## Slide 3
Introduction

## Slide 4
Introduction
15 billion IoT devices in the world
MAC layer : 2nd layer of OSI model
Requirements :
- Coverage area
- Scalability
- Data rate
- Latency
- Energy efficiency
- Security
IoT fields
Industrial
Security
Logistic / fleet managment
Traffic control
Remote monitoring
Robotics

## Slide 5
MAC layer definition

## Slide 6
MAC layer definition
MAC : “Medium Access Control” => subset of Data Link layer
Control access to physical transmission medium
MAC : “Medium Access Control” => subset of Data Link layer
Various tasks :
Addressing : assign unique MAC addresses
Error detection : ensure integrity of transmitted data
Frame management : create frames with data from above layers
Frame filtering : assure received frames are for you
Access control : how the node have access to medium (methods like CSMA/CA)
Contention-based
Synchronous
Asynchronous
Scheduled-based
TDMA
FDMA

## Slide 7
Contention-based protocols
Synchronous :
Asynchronous :
Compete to access the medium
Example : S-MAC protocol
Advantages :
Mobility
Can be couples to CSMA/CA to avoid collision (need more energy)
Disadvantages :
Listen to often => bad energy efficiency
Hard scalability => lot of collision
Lot of synchronization packets (collision & energy consumption)
Based on low-power listening + preambles frames
Example : WiseMAC protocol
Advantages :
No explicit synchronization
Reduce Idle of receiver
More flexible changes than synch’
Disadvantages :
Does not deal with collision
Increase latency
Over-emitting transmitter before data

## Slide 8
Scheduled-based protocols
FDMA :
TDMA :
Example : MMSN protocol
Advantages :
Low mobility => good node localization
Negligeable overhead => energy saving
Collision avoidance
Predictable latency
More than one node can send/receive at a time
Disadvantages :
Low node mobility
Hard topology changes
Complex synchronization
Example : Energy & Rate protocol
Advantages :
No packet loss
Voting phase => save bandwidth & reduce overhead
Energy efficient for high data traffic
Disadvantages :
Low node mobility
Node can only communicate during its slot => can lead to low bandwidth use

## Slide 9
Conclusion

## Slide 10
Conclusion
4 types of MAC layer protocols :
Contention-based
Synchronous
Asynchronous
Scheduled-based
TDMA
FDMA
No scheduling => can use all the bandwidth
Need synchronization or listening to the medium => energy consuming
Allows more node mobility / network topology changes
Security not really implemented, relies on other layers
Can be better than scheduled in term of energy efficiency for moving networks (add and sub of nodes)
Scheduling => low bandwidth in some use cases
Need synchronization only at the beginning => efficient if the topology don’t move to much
Bad for nodes mobility / network topology changes
Security not really implemented, relies on other layers
Can be better than contention in term of energy efficiency for fixed networks (less packages sent for sync and so on)